FOS-3126-PLUS SKA

Quick Configuration Guide

| Revision History: |
| --- |
| 1. | Created by Franklin Hsieh | 2008-11-28 |
| 2. |  |  |

Content:

A. DHCP Snooping Configuration Procedure

- Environment

- Setup Procedure

Step 1 Enable the DHCP Snooping function.

B. DHCP Option82 Configuration Procedure

- Environment

- Setup Procedure

Step 1 Enable the DHCP Option82 function.

C. IPv6 Filter Configuration Procedure

- Environment

- Setup Procedure

Step 1 Enable the IPv6 Filter function.

D. UPnP Filter Configuration Procedure

- Environment

- Setup Procedure

Step 1 Enable the UPnP Filter function.

E. Mal-attempt Syslog Configuration Procedure

- Environment

- Setup Procedure

Step 1 Setup the Mal-attempt Syslog function.

F. Source IP Anti-Spoofing Configuration Procedure

- Environment

- Setup Procedure

Step 1 Setup the Source IP Anti-Spoofing function.

Step 2 Setup the Static IP Mapping for a Port.

A. DHCP Snooping Configuration Procedure

Environment:

| Interface | MAC_Addr | IP_Addr |
| --- | --- | --- |
| #4 | xx:xx:xx.. | 192.168.1.3 |
| ... | ... | ... |

Setup Procedure:

Access FOS-3126-PLUS by “Telnet” or “RS-232” console with the following username and password:

Username: Admin ↵

Password: ↵

Figure 1. FOS-3126-PLUS Login Menu page

- Enable the DHCP Snooping function.

Follow the following path to enter the DHCP Port Settings page as show in Figure 2.

  - 4. Switch Management

  - D. SKA Configuration

  - 2. DHCP Port Settings

And select the DHCP mode as show in Figure 2.

Figure 2. DHCP Port Settings page

PS. The Uplink Port for DHCP Server FIX in Port 25 or Port 26

B. DHCP Option82 Configuration Procedure

Environment:

Setup Procedure:

- Enable the DHCP Option82 function.

Follow the following path to enter the DHCP Opt82 Settings page as show in Figure 3.

  - 4. Switch Management

  - D. SKA Configuration

  - 1. DHCP Opt82 Settings

And enable the DHCP Opt82 Relay Agent as show in Figure 3.

Figure 3. DHCP Opt82 Settings page

PS. DHCP Snooping needs to enable to make the Option82 work.

C. IPv6 Filter Configuration Procedure

Environment:

Setup Procedure:

- Enable the IPv6 Filter function.

Follow the following path to enter the Filter Configuration page as show in Figure 4.

  - 4. Switch Management

  - D. SKA Configuration

  - 3. Filter Configuration

And enable the IPv6 auto discovery / DHCPv6 as show in Figure 4.

Figure 4. Filter Configuration page

D. UPnP Filter Configuration Procedure

Environment:

Setup Procedure:

- Enable the UPnP Filter function.

Follow the following path to enter the Filter Configuration page as show in Figure 5.

  - 4. Switch Management

  - D. SKA Configuration

  - 3. Filter Configuration

And enable the UPnP Filter as show in Figure 5.

Figure 5. Filter Configuration page

E. Syslog Configuration Procedure

Environment:

| Interface | MAC_Addr | IP_Addr |
| --- | --- | --- |
| #4 | xx:xx:xx.. | 192.168.1.3 |
| ... | ... | ... |

Setup Procedure:

- Setup the Mal-attempt Syslog function.

Follow the following path to enter the Mal-attempt Log Configuration page as show in Figure 6.

  - 3. Network Management

  - 8. Mal-attempt Log Configuration

Enable the Log Server and enter the Log Server IP as show in Figure 6.

Figure 6. Mal-attempt Log Configuration page

F. Source IP Anti-Spoofing Configuration

Environment:

| Interface | MAC_Addr | IP_Addr |
| --- | --- | --- |
| #4 | xx:xx:xx.. | 192.168.1.3 |
| ... | ... | ... |

Setup Procedure:

- Setup the Source IP Anti-Spoofing function.

Follow the following path to enter the DHCP Port Settings page as show in Figure 7.

  - 4. Switch Management

  - D. SKA Configuration

  - 2. DHCP Port Settings

And select the FIX-IP mode as show in Figure 7.

Figure 7. DHCP Port Settings page

- Setup the Static IP Mapping for a Port.

Follow the following path to enter the Static IP Table Configuration page as show in Figure 8.

  - 4. Switch Management

  - D. SKA Configuration

  - 4. Static IP Table Configuration

Creates “static IP-Port” mapping as show in Figure 8.

Figure 8. Static IP Table Configuration page

# Text boxes

DHCP Offer, ACK

DHCP_pkt

MC-Addr

DHCP_pkt

Op-82

Drop

DHCP Discover, Request

DHCP Server

DHCP Offer, ACK

DHCP_pkt

MC-Addr

DHCP_pkt

MC-Addr

DHCP Server

Drop

Customer

Premises

PC2

Customer

Premises

PC1

Customer port

Uplink port

MC-Addr

DHCP_pkt

Op-82

MC-Addr

DHCP_pkt

MC-Addr

DHCP Server

DHCP Discover, Request

Customer

Premises

PC1

Customer port

Uplink port

UPnP_pkt

IPv4

MC-Addr#A

UPnP_pkt

IPv6_pkt

MC-Addr#A

IPv6_pkt

MC-Addr#A

IPv6 Router

Drop

IPv6

Customer

Premises

PC2

Customer

Premises

PC1

Customer port

Uplink port

IPv4

MC-Addr#A

Router

Drop

UPnP

Customer

Premises

PC2

Customer

Premises

PC1

Customer port

Uplink port

TCP/IP

MC-Addr

Drop

ARP Spoofing

Syslog_pkt

MC-Addr

Syslog Server

Source IP Not Match

Drop

Customer

Premises

PC2

Customer

Premises

PC1

Customer port

Uplink port

DHCP Client

Spoof IP

Source IP Not Match

TCP/IP

MC-Addr

TCP/IP

MC-Addr

Router

Drop

Customer

Premises

PC2

Customer

Premises

PC1

Customer port

Uplink port